## Slide 1: A deferred material rendering system
Tomasz Stachowiak
@h3r2tic

## Slide 2: Motivation
Render the whole scene with a handful of draw calls
Shade only the visible pixels
Reduce pixel work in geometry-heavy passes
  Less overshading tax
Allow control over shading rate
Support exotic sample generation
  Ray-tracing
  Texture-space shading
  Arbitrary points in space

## Slide 3: Inspiration
The Visibility Buffer: A Cache-Friendly Approach to Deferred Shading
  Christopher A. Burns and Warren A. Hunt
TL;DR: /* massive simplification */
Render a super thin attribute buffer
  Instance ID, Primitive ID
For each pixel
  Fetch primitive from the IDs
  Manually interpolate attributes from vertices
  Shade
  … just like a ray-tracer would after having found the intersection!

## Slide 4: My contributions
Making barycentric coordinates part of the V-Buffer
  No need for ray-triangle intersection
  Mesh animation doesn’t require stream-out
  Fatter V-Buffer than Intel’s
Scaling to thousands of materials
Disclaimer: GCN-centric
  Similar ideas could be made to work on non-GCN

## Slide 5: Rendering barycentric coordinates
Vertex stream with {0, 1}, {0, 1}, {0, 0}, … ?
  Needs duplicate vertices -> breaks vcache, ~2x slower
Geometry shader?
  ~2x slower
Domain shader?
  ~2x slower
Intersect primitive per pixel?
  Need to stream-out vertex animation
GCN has a trick up its sleeve 

## Slide 6: GCN recap: smooth parameter interpolation
in smooth float param;
out vec4 outColor;
void main() {
outColor = param.xxxx;
}
S_MOV_B32 M0, s2
V_INTERP_P1_F32(a0.X) v0 = P10 * v0 + P0
V_INTERP_P2_F32(a0.X) v0 += P20 * v1
V_CVT_PKRTZ_F16_F32 v0, v0, v0
S_NOP(1)
EXP_FP16 v0, v0, v0, v0 (MRT0,VM,DONE)
S_ENDPGM

## Slide 7: GCN recap: flat parameter interpolation
in flat float param;
out vec4 outColor;
void main() {
outColor = param.xxxx;
}
S_MOV_B32 M0, s2
V_INTERP_MOV_F32(a0.X) v0 = P0
V_CVT_PKRTZ_F16_F32 v0, v0, v0
S_NOP(1)
EXP_FP16 v0, v0, v0, v0 (MRT0,VM,DONE)
S_ENDPGM

## Slide 8: V_INTERP_Px_F32
V_INTERP_P1_F32(a0.X) v0 = P10 * v0 + P0
V_INTERP_P2_F32(a0.X) v0 += P20 * v1
Given:
  A parameter of three vertices: P0, P1, P2
  Barycentric coordinates: I, J
  P10 = P1 – P0
  P20 = P2 – P0
Final value = P0 + P10 * I + P20 * J
P0
P1
P2
P10
P20
  I, J

## Slide 9: V_INTERP_MOV_F32
V_INTERP_MOV_F32(a0.X) v0 = P0
Final value = P0
Same as
  V_INTERP_P1_F32 + V_INTERP_P2_F32
  with I, J == 0
P0

## Slide 10: Pixel shader tampering
Start with a simple one:
Modify ISA
???
PROFIT!
S_MOV_B32 M0, s2
V_MOV_B32 v2, 0
V_MOV_B32 v3, 1.0
V_INTERP_P1_F32(a0.X) v0 = P10*v0 + P0
V_INTERP_P2_F32(a0.X) v0 += P20*v1
V_CVT_PKRTZ_F16_F32 v0, v0, v2
V_CVT_PKRTZ_F16_F32 v1, v2, v3
EXP_FP16 (...)
S_ENDPGM
S_MOV_B32 M0, s2
S_NOP(1)
S_NOP(1)
S_NOP(1)
V_MOV_B32 v2, v1
V_CVT_PKRTZ_F16_F32 v0, v0, v2
V_CVT_PKRTZ_F16_F32 v1, v2, v3
EXP_FP16 (...)
S_ENDPGM
in smooth float param;
out vec2 outColor;
void main() {
outColor = vec2(param, 0);
}
  I, J

## Slide 12: Uh, that almost worked
GPU reorders vertices at Primitive Assembly*
  Some sort of slope dependency
  Clipping affects it too
  I haven’t identified a simple rule yet
  Winding order stays the same
    Three possible rotations
  *thanks, Fabian!
Barycentric coords are reordered to match
  Thus pixel shader doesn’t care
We need them to correspond to original mesh data

## Slide 13: But wait…
We can use V_INTERP_MOV_F32 to get P0
  … and it will be a different vertex depending on rotation
Yet flat parameters also use V_INTERP_MOV_F32
  … and it’s always the provoking vertex
    GL_LAST_COORD_CONVENTION by default
Behavior depends on interpolation qualifier
  flat or smooth

## Slide 14: Re-orienting the barycentrics
Export the same parameter twice
  out flat float Flat;
  out smooth float Smooth;
if P0.Smooth == P0.Flat
Correct orientation!
if P1.Smooth == P0.Flat
Rotate by 1
else
Rotate by 2

## Slide 15: Example implementation
V_SUB_F32 v0, 1.0, v0
V_SUB_F32 v0, v0, v1
V_INTERP_MOV_F32(a0.Z) v2 = P0
V_INTERP_MOV_F32(a2.Z) v3 = P0
V_CMP_EQ_F32 VCC, v2, v3
V_SUB_F32 v4, 1.0, v0
V_SUB_F32 v4, v4, v1
V_CNDMASK_B32 v0, v0, v1
V_CNDMASK_B32 v1, v1, v4
V_MOV_B32 v4, 1.0
V_INTERP_P2_F32(a0.Z) v2 += P20*v4
V_CMP_EQ_F32 VCC, v2, v3
V_SUB_F32 v2, 1.0, v0
V_SUB_F32 v2, v2, v1
V_CNDMASK_B32 v1, v1, v0
V_CNDMASK_B32 v0, v0, v2
Look Ma, no geometry or domain shaders!
Export gl_VertexID as the parameter in VS
Works with indexed draws
Ludicrous speed!
…but can we have barycentrics without hacks, dear IHVs? 
Change winding order to CCW

## Slide 17: Deferred material shading – overview
Render an attribute buffer
  Instance ID, Primitive ID, Material ID, Barycentric U & V
    Material ID optional
    Barycentric coords typically need more than 16-bit/component
  Single RGBA32F
Bin pixels per material
  Store pixel screen coords
Dispatch material shaders

## Slide 18: Binning pixels per material
Naïve idea: append buffer per material
  O(materials * pixels) memory requirements 
One append buffer then!
Add pixels in any order, sort later?
  Sloooooooooooooow

## Slide 19: Counting sort to the rescue
Count pixels using each material O(pixels)
  Use global atomics
Exclusive prefix scan pixel counts O(materials)
  dst[i] = src[0] + src[1] + … + src[i-1]
Write each pixel to target bin O(pixels)
Count |  |  |  | 
Prefix scan | 0 | 7 | 31 | 46
 | 7 | 24 | 15 | 18

## Slide 20: Global atomic pressure in counting
Crazy contention if pixels use few materials
Run in 8x8 tiles via compute
Find squares of identical materials
  Hierarchical reduction
Global atomic add on detected squares
  Only one if the tile uses a single material 
Internal index via LDS atomics
~1ms -> ~0.18ms
  720p, Tonga (R9 285)
  Not really optimized otherwise

## Slide 21: Dispatching material shaders
One dispatch indirect per material?
  Material count could be very high
  Abuses the command processor
  Might be fine for some use cases!
Ubershader?
  The compiler won’t be amused
  Pay for the worst case
Shader jump table?
  Compile all shaders separately
  Dump ISA into a buffer (See “Hacking GCN via OpenGL”)
  Dispatcher shader reads material ID, jumps using S_SETPC_B64

## Slide 22: Making it more efficient
Dispatcher shader must have worst-case resource allocation
  VGPR, SGPR, LDS
In practice: occupancy of 1 
Group shaders by max occupancy!

## Slide 23
Waves/SIMD | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Max VGPRs | 24 | 28 | 32 | 36 | 40 | 48 | 64 | 84 | 128 | 256
Max SGPRs | 48 | 56 | 64 | 72 | 80 | 96 | 102 | 102 | 102 | 102

## Slide 24: So how about ten dispatcher shaders?
Check the SGPR, VGPR, and LDS usage of each material shader
Bin it depending on max occupancy
  Exactly ten bins
Create a shader for each bin
Pre-sort materials by bin
Shade everything with ten dispatches
  Still just one sub-allocated pixel list
Now shading at proper occupancy

## Slide 25: But wait, those materials aren’t compatible!
If two shaders use different resources, we can’t merge them
  Say, one needs no textures
  Another uses a normal map and a diffuse texture
Or else.

## Slide 26: BINDLESS
ALL THE THINGS!

## Slide 27: One resource to rule them all
layout(std140, binding = 0) uniform BindlessResources
{
usamplerBuffer ClassificationResult;
usamplerBuffer WorkgroupData;
usamplerBuffer GlobalIndexBuffer;
usamplerBuffer GlobalVertexBuffer;
…
};

## Slide 28: Unfortunately that’s a bit ugly…
Can haz buffer pointers, GLSL?
  NV_shader_buffer_load is so much nicer!
uvec3 fetchTriangleIndices(int offset)
{
usamplerBuffer buf = GlobalIndexBuffer;
if (0 == (offset & 3)) {
return texelFetch(buf, offset >> 2).xyz;
} else if (1 == (offset & 3)) {
return texelFetch(buf, offset >> 2).yzw;
} else if (2 == (offset & 3)) {
return uvec3(texelFetch(buf, offset >> 2).zw, texelFetch(buf, (offset >> 2) + 1).x);
} else {
return uvec3(texelFetch(buf, offset >> 2).w, texelFetch(buf, (offset >> 2) + 1).xy);
}
}

## Slide 29: … but it gets the job done
The ugly sits in wrapper functions
All material shaders now compatible
  Only one resource
  No descriptor table necessary
    Buffer descriptor right in SGPRs
    Good job, driver!
Render everything with:
  1 draw call
    … or however many vertex shaders you have
  16 compute dispatches
    6 for classification and work generation
    10 for materials

## Slide 30: Let’s test it, shall we?
Should be able to support thousands of materials
Difficult to get representative shaders
  At least out in the open :P
I could write a few, but I need to sleep sometimes

## Slide 31
Oh, look, Shadertoy has a web API :D
  Can fetch us all the public shaders
  Resources, code, meta info
Grab the purely procedural ones for now
  Could support texture inputs just fine
Some fail to compile
  Derivatives
  Audio channels
  WebGL compatibility issues
  Skip them

## Slide 36: Making of the Shadertoy Metaverse®™™
892 shaders compile without errors
Dump ISA from all shaders into a single buffer
  ~14 MB worth of GCN code
Render a grid of 892 cubes
  Could be one draw call
  Only difference: written material ID
16 compute dispatches render all the materials

## Slide 37: Shadertoy Metaverse®™™ takeaways
No overshading in the material pass
  Other inefficiencies (cache coherency, etc.)
  No need to sort front-to-back
Mostly just worked
  A few shaders have artifacts
    More homework
Shader compilation takes a while
  Can serialize ISA and later bypass GL altogether

## Slide 38: 892 cubes in a grid look like a mess…
… so let’s see just 64 Shadertoys in a video!
Note: I didn’t write any of those;
many awesome people did!

## Slide 40: Bonus: variable-rate shading
Quite easy to do in the framework
Classification pass controls shading rate
Example:
  if (same material && similar depth in 2x2 tile) {
  if ((pixel.x | pixel.y) & 1) {
  skip pixel;
  } else {
  add pixel as 2x2 tile;
  }
  }

## Slide 41: Issues
Alpha tested-rendering
  Mask textures still needed in the geometry pass
No transparency support
  Per pixel linked lists?
GPU underutilized during geometry pass
  Run some async compute!
No automatic derivatives
  Calculate analytically (expensive)
  Finite-differencing permutation for 2x2 tiles?

## Slide 42: Where to next?
Shading samples can be generated by anything
  Only barycentric coords, instance ID, and primitive ID are needed
  Ray-tracing?
  Texture space?
    I want a modern surface cache!
Lots of room for optimization and research
  Group by primitive, prefetch params into LDS
  Pack shading samples spatially for memory coherency
  Can the HW scheduler mix low-VGPR/hi-SGPR shaders with hi-VGPR/low-SGPR?
Smarter variable-rate shading

## Slide 43: Extension: Fractional rendering
Variable rate simple with deferred material shading
Pixel work explicitly created in classification pass
  if (someCondition) schedulePixelShading(x, y);
Spatial
  Schedule pixels sparsely
  Fill in gaps
Temporal
  Schedule pixel if rand() > k
  Reproject gaps

## Slide 44: if (rand() > k)

## Slide 45: + Temporal reprojeciton

## Slide 46: + Whoops

## Slide 47: + Explicit disocclusion handling

## Slide 48: Foveated rendering
Vary random threshold over image
Radial distance to screen center
Average shading cost (rate) is 1/5 in this case

## Slide 49: Temporal + spatial
Disocclusions can be significant
  Camera cuts, nearby objects
  All pixels in the worst case
Shade disocclusions at quarter-rate
  Almost the same quality in practice
  1/4th of the cost
  Same idea as before
  Splat the same color to 2x2 pixel blocks

## Slide 50: Quarter-rate disocclusions

## Slide 51: What is it good for?
View independent-stuff
  Diffuse lighting
  AO
  G-Buffer parameters
  Primary artifact is blurriness
High frequency specular breaks it
  Predict it and shade at higher rate?
  Do spec separately?
  Shade adaptively?
Credit: Hugo Elias (Radiosity)

## Slide 52: Thanks!